## Slide 1: Microarchitecture of Superscalar Processor
James E. Smith, Gurindar S. Sohi
by, TEJESHWARA B M
24th October 2016

## Slide 2: Elements of High Performance Processing
Fetch multiple instructions.
Methods for determining true dependences, during execution.
Initiating, or issuing, multiple instructions in parallel.
Communicating data values through memory via load and store instructions.
Committing the process state in correct order.

## Slide 3
Control dependency constraints
When there is a conditional branch or jump, the program counter may be updated to a non-consecutive address. An instruction is said to be control dependent on its preceding dynamic instruction(s).
To overcome from control dependency, a method for is to predict the outcome of a conditional branch and speculatively fetch and execute instructions from the predicted path.

## Slide 4
Speculative execution
means that some instructions may complete execution
when they would not have executed at all had the sequential model been followed
Architectural storage (the storage that is outwardly visible)
It cannot be updated immediately when instructions complete execution.
Rather, the results of an instruction must be held in a
temporary status until the architectural state can be updated.

## Slide 5: Data dependency constraints
TRUE dependency : RAW
Artificial dependency : WAW, WAR

## Slide 6: Organisation of Superscalar Processor

## Slide 7: 1. IF and Branch Prediction
Instruction cache
Data cache
1. Recognizing conditional branches
pre-decode
2. Determining the branch outcome
static information : loops
dynamic information : branch history,
dynamic table, speculation
3. Computing branch targets
PC (uses offset value)
4. Transferring control
stockpile – mask the delay
buffers
:Stockpile :
An instruction buffer to hold a number of fetched instructions. The fetch mechanism can build up a "stockpile"

## Slide 8: 2. Decoding, Renaming & Dispatch
This phase includes detection of true data dependences
Resolution of other register hazards,
e.g. WAW and WAR

## Slide 9
Register renaming
- logical register
- physical register
2. Reordered buffer
- FIFO
Register renaming eliminates artificial dependences due to WAW and WAR hazards.
Leaving only the true RAW register dependences.

## Slide 10: 3. Instruction Issuing and Parallel Execution
Constraints:
Execution unit
Interconnect
Register ports
Issue buffer

## Slide 11
Single Queue Method
  out-of-order issue
  register renaming
  reservation bits
Multiple queue Method
  FP instruction Q
  INT instruction Q
  LD/ST instruction Q

## Slide 12
Reservation Stations
  no strict FIFO
  uses pointers instead of source data
  Proposed in Tomasulo’s algorithm

## Slide 13: 4. Handling Memory Operation
Address translation
Translation lookaside buffer (TLB)
Rename
Multiported
Store address buffer

## Slide 14
5. Committing state
6. Role of Software
Sequential execution
Precise state
Techniques of recovery
  Checkpoint/history buffer
  Physical state
  Logical/architectural state (reordered buffer, register renaming)
Software Scheduling
  Group of instruction should issued more
  Dependency of prev instruction should make minimum

## Slide 15: MIPS R10000

## Slide 16
 | MIPS R10000 | Alpha 21164 | AMD K5
Theme | 4 - way superscalar | 4 - way superscalar | variable length instruction
Pre-decode bits | 4 | 0 | 5
Branch prediction | resume cache | branch history entry (2 bits) | using pointers
Functional unit | 1 - address adder 1 - FP adder 1 - FP M/D/Sqrt 2 - interger ALU | 1 - FP adder 1 - FP Multiplier 2 - interger ALU | 1 - FP unit 1 - branch unit 2 - interger ALU 2 - LD/ST units
Features | * Branch snapshot * physical reg = 2 x Logical reg * exception handling - reorderbuffer * 4 commits at a time | * high clock rate * miss address file(MAF) - 6 entry * Bypass in reorderbuffer * No out-of-order | 

## Slide 17: Alpha 21164

## Slide 18: AMD K5

## Slide 19: Conclusion
Limitation
  Conditional branches
  Complexity in simultaneous issuing instruction
  Gap btw processor & main memory
    Sophisticated data cache
    Better cache prefetch method
    More developed memory hierarchy
    Memory chip design
    8-way superscalar

## Slide 20: What next ….?
VLIW : It’s collection of several independent operations, which can all be executed in parallel.
  s/w being responsible for analysing dependency & creating execution schedule.
  Hardware utilisation is lesser & simpler to implement.
Multiprocessor
  Inter processor synchronization & communication overhead extremely low.
  Flow control mechanism.

## Slide 21
THANK YOU